## Slide 1: System-Level Design of Adaptive Wireless Transceivers including Antenna Arrays
Tim Reeves Application Engineer

## Slide 2: What material are we going to cover today?
Three topics that we are going to cover today, each session is one hour long covering the following topics:
  Top down design of RF transceivers: From spreadsheet computations to fast RF simulation
  Antenna and antenna array design for wireless engineers
  End-to-End Modelling of Wireless Systems

## Slide 3: What sort of system model could ultimately be developed using MathWorks tools?

## Slide 4: What are some of the key things included in this model?
Antenna Modeling:
  Isolated element and superposition principles used in modeling the receive array.
  Antenna element interaction as well as impedance loading included in receive array
RF Modeling:
  RF receiver model that includes, linear, non-linear and noise behavior
  Matching network for receive antennas
  RF components described by measured data (S-parameters)
Beamforming:
  Baseband DSP algorithms used to determine error rates and determine beamforming angles

## Slide 5
Part One:
  Top down design of RF transceivers: From spreadsheet computations to fast RF simulation

## Slide 6: How do MathWorks Tools Integrate into a “Top-Down” Communications System Design Flow?
INTEGRATION
IMPLEMENTATION
DESIGN
TEST & VERIFICATION
FPGA
ASIC
VHDL, Verilog
RF
SMPS
Spice-like
Algorithms
Analog
Digital
Physical
Fixed-Point
SPECIFICATION
Multi-domain algorithm development
Elaborate ‘Golden’ reference model derived from specification
Study architectural trade-offs between analog and digital systems
Determine integrated system performance
Verification
Co-simulation with 3rd party tools
Testbench generation
Integration with test and measurement equipment
Implementation and prototyping
Architectural models that are representative of board level implementations.
Synthesizable HDL code generation
Notes: How do MathWorks Tools fit in the overall mixed-signal design and verification space?
First of all, MathWorks provide a platform for system-level design and simulation. MathWorks tools are complementary to the tools used for IC implementation (Cadence, Synopsys, Mentor Graphics) and do not provide an alternative to these tools.
MathWorks tools provide a natural environment for building multi-domain system-level models, integrating analog, digital, mixed-signal, RF and supervisory logic expressed as HW or SW. A large set of libraries and a fast simulation environment make easier to build system-level models making use of graphical and textual entries for maximum expressivity.
Naturally MATLAB and Simulink provide an environment to build behavioral models and validate the real-number abstraction. These models can then be brought downstream for integration in the verification workflow.
MathWorks tools link to the downstream tools by means of cosimulation or code-generation. This supports the validation of the system-level behavioral models against the IC implementation, and allows building expressive system-level testbenches for the mixed-signal IP verification.
The link with the test and measurement equipment and the ability to use FPGAs for rapid prototyping provide even more tools for rapidly verifying the models and validate the IC.
Automatic code generation for digital HW and SW/Firmware provide a fast route towards implementation for the part of the design that support automatic model transformation (obviously not the analog part).

## Slide 7: How do we integrate RF Behavior with MathWorks tools?
Integrating RF behavior into Communications system models will likely be your biggest integration challenge.
RF behavior is included via a physical modeling platform that is an addition to Simulink.
RF systems are realized in a manner similar to that of circuit simulators that you would find in Cadence Virtuoso, KeySight’s ADS circuit simulator etc..

## Slide 8: What part of the design do we want to begin with?
You often start with an Excel Spreadsheet for doing Budget calculations; let’s do this with a new MATLAB application, RF Budget Analyzer
What benefit does it bring to you?
  Implements power / noise / IP3 RF link budget analytical computations
  Better than similar custom-made spreadsheets – takes into account mismatches
  Generates models / testbenches for SimRF Circuit Envelope simulations
  Provides consistency between analytical and simulation results
  Supports the “top-down” design workflow

## Slide 9
Add RF components
Export to SimRF
Cascade Budget Analysis
Component specifications
RF Cascade
Notes: RF Budget Analyzer
Once you start the app, you can add components and build a high level chain. You can specify the data sheet parameters of the components, or import measurements such as 2-port Touchstone files.
The app computes the power/noise/ip3 budget at each stage of the chain taking into account impedance mismatches. This allows the designers to decide how to partition the system and define the high-level specs of the different components.
When the analysis is completed and deemed satisfactory, you can automatically generate a SimRF model to validate the system performance using simulation.
This allows you to integrate RF front-end into more complex systems, adding signal processing and control algorithms and testing the RF front-end in different scenarios. Moreover the RF model can be extended to describe the RF architecture in a more accurate way, or by adding imperfections that cannot be taken into account using analytical computations.

## Slide 10: How do I export a SimRF model?
The application has an option to export a simple Simulink testbench to measure power and gain
Tstop = 0  static analysis (harmonic balance)
Input/output ports and RF configuration are setup correctly
Copy and paste to include RF model in more complex set ups
Notes: Export to SimRF
You can build a simple SimRF testbench to validate expected gain and power levels of your chain. The automatically generated model can be easily embedded into more complex system
models.
Notice that the input/output ports are set up with the correct frequencies, and the configuration block uses a very wide simulation bandwidth. Notice also that the modulator/demodulators integrate ideal image rejection filters to reproduce the analytical results. When the RF designers implement these blocks they will have to design the filters accordingly.
In order to speed up simulation, you might want to reduce the harmonic order or to reassess the simulation bandwidth. As this depends on the actual power level of the input signal and on the operating conditions, this is not something that SimRF can automatically do.

## Slide 11: How can I verify that my SimRF model reproduces the expected theoretical results?
There is also an option to generate a more sophisticated Simulink testbench to measure gain, noise and IP3 using time domain simulation
When making noise measurements, follow the same practices that you would in the lab, i.e. make sure that you use narrow-band simulation to get accurate narrowband results (e.g. spot noise)
You will be able to validate that the RF front end is behaving as expected
Notes: Export to SimRF Testbench
This testbench is a bit more involved and requires DSP System Toolbox. With this testbench you can measure the gain, noise and IP3 of the chain. You can also inspect and understand how these measurements are done in the time domain.
In case of filtering elements, the gain, noise and IP3 will depend on the bandwidth of the measurement. For this reason, you might have to decrease the bandwidth of the signal measurement in order to measure spot (narrowband) properties.

## Slide 12: Let’s start with understanding how to do RF System modeling in Simulink
What would you like to be able to do with a RF behavioral modeling tool?
  Design and define both the architecture and the specs of the RF components
  Test and debug the implementation of the transceiver before going in the lab
  Integrate RF front ends with adaptive algorithms such as DPD, AGC
  Provide a model of the RF transceiver to your colleagues and customers

## Slide 13: What do you need from a RF System Simulator?
RF and analog behavioral models that capture linear, non-linear and noise performance
Ability to develop control, calibration and signal processing algorithms
Fast simulation of baseband + RF systems
Radio Frequency
Signals
Small simulation time-step
Long Simulation Runs
~10psec
~5GHz

## Slide 14: Section Wrap-up
We discussed how MathWorks tools can be used in a “top-down” design workflow for RF systems and how that workflow tightly corresponds to commonly used design flows, in that:
    You have access to a MATLAB application that allows you to compute RF budgets in a manner that is comparable to work that you do with Excel spreadsheets.
    From this MATLAB application, you can generate Simulink-based RF systems for use in larger communication system simulations.
    You also have the option to generate Simulink test benches that generate RF Budget results that compare favorably to the analytical results.

## Slide 15: Let’s revisit our system model that we were looking at before.

## Slide 16
Part Two:
  Antenna and antenna array design for wireless engineers

## Slide 17: How can I model antennas using MathWorks tools?
Antenna Toolbox
Easy design
  Library of parameterized antenna elements
  Functionality for the design of antenna arrays
  No need for full CAD design
Rapid simulation setup
  Method of Moments field solver for port, field, and surface analysis
  No need to be an EM expert
Seamless integration
  Model the antenna together with signal processing algorithms
  Rapid iteration of different antenna scenarios for radar and communication systems design

## Slide 18: Antenna Toolbox Demo Design and analysis of one antenna element, in just 5 lines of MATLAB code
>> p = patchMicrostrip
>> p.Height = 0.01;
>> impedance(p, (500e6:10e6:2e9));
>> current(p, 1.66e9);
>> pattern(p, 1.66e9);

## Slide 19: What radiating structures are part of Antenna Toolbox?
Dipole antennas
  Dipole, Vee, Folded, Meander, Triangular bowtie, Rounded bowtie
Monopole antennas
  Monopole, Top hat, Inverted-F, inverted-L, Helix
Patch antennas
  Microstrip patch, PIFA
Spirals
  Equiangular, Archimedean
Loops
  Circular, rectangular
Backing structures
  Reflector and cavity
Other common antennas
  Yagi Uda, Slot, Vivaldi, Biquad, Horn

## Slide 20: What if my Antenna is not included in the Library?
Define your custom planar structure
  Define the antenna geometry using PDE Toolbox
  Define the mesh using MATLAB delaunayTriangulation
  Use third party tools to generate a mesh structure
Import 2D mesh with Antenna Toolbox
  Define the feeding point
  Analyse the antenna
Integrate your custom antenna
  Define a backing structure
  Define a dielectric structure
  Build an array with custom elements

## Slide 21: What if my Antenna is Mounted on a Dielectric Substrate?
Antenna are often mounted on substrates
Dielectric properties:
Dielectric properties affect resonant frequency, bandwidth, efficiency, pattern …
Use the dielectric catalogue listing existing materials
Define your own dielectric material
Dielectric | Relative permittivity | Loss Tangent
Air | 1 | 0
Other | >1 (typically <10) | >0 (typically ~1e-3)
“metal” antenna
(ideal conductor)
Free space (isolation)
Dielectric substrate

## Slide 22: How can I efficiently include dielectric properties while not dramatically increasing my design time?
Modelling the dielectric substrate can slow down analysis time:
Use antennas in free space for first-cut design
  Combine with optimization routines to rapidly determine a suitable starting point
Use parallel computing to speed up wideband frequency analysis
Poor directivity
Optimized pattern

## Slide 23: How are results obtained using Antenna Toolbox incorporated into the downstream workflow?
Field (Antenna behaviour)
  Radiation Pattern, Beamwidth, E-Plane and H-Plane, Polarization, Axial Ratio
Port (RF / Microwave behaviour)
  Input Impedance, Resonance, Reflection Coefficient, Return Loss, Voltage Standing Wave Ratio (VSWR), Bandwidth

## Slide 24: What if you Need to Take into Account …
Coupling effects in between antenna elements?
Edge effects?
Pattern multiplication of the isolated element is not sufficient!
Full wave
Isolated element
pattern superposition
Comparison

## Slide 25: How can I construct an Antenna Array using Antenna Toolbox?
>> a = linearArray
>> a.Element = p;
>> a.ElementSpacing = 0.1;
>> a.NumElements = 4;
>> show(a);
>> patternElevation(a, 1.66e9,0);

## Slide 26: What if I Need to Customize my Array?
Build regular arrays where you can change the properties of individual elements (rotation, size, tapering)
Describe conformal (heterogeneous) arrays in terms of element type and arbitrary position
>> arr = conformalArray;
>> d = dipole;
>> b = bowtieTriangular;
>> arr.Element = {d, b};
>> arr.ElementPosition(1,:) = [0 0 0];
>> arr.ElementPosition(2,:) = [0 0.5 0];

## Slide 27: Why do I want to import an antenna element pattern into Phased Array system toolbox?
An isolated antenna element pattern can be imported into Phased Array system toolbox to estimate the array pattern
Phased Array System Toolbox provides algorithms and tools to design, simulate, and analyze phased array signal processing systems
  Beamforming
  Estimation of Direction of Arrival
...
% Import antenna element in Phased Array
>> myantenna = dipole;
>> myURA = phased.URA;
>> myURA.Element = myantenna;
Antenna element (isolated)
Phased Array System Toolbox
antenna array

## Slide 28: Modelling the Array Radiation Pattern in Practice
Are the antenna elements spaced far apart?
Mid
Compute the pattern for the central and the edge (corner) element embedded in the array
Compute the isolated element pattern and apply pattern superposition
yes
What is the size of the array?
no
Small
Compute the pattern for each element embedded in the array
<10
Heterogeneous array
Validate (when possible)
with full EM simulation
Homogenous array
>10x10
Large
Compute the pattern for the central element with the infinite array approach

## Slide 29: How can I model element interaction without doing fullwave EM simulation?
Calculate the embedded element pattern and use the same concepts as mentioned before for doing pattern multiplication.
pattern(l, 10e9, ...
'ElementNumber',2);
Embedded element
pattern(l, 10e9);
Full wave

## Slide 30: What if my Array is Really Large?
Infinite Array Analysis
  Repeat unit cell infinitely
  Impedance and pattern become function of frequency and scan angle
  Ignore edge effects
  Captures mutual coupling
Validate with full wave simulation on smaller arrays
Scan Impedance @10GHz
0deg Azimuth
45deg Azimuth
90deg Azimuth
Scan Impedance
0deg Azimuth 45deg Elevation
Power Pattern

## Slide 31: Where can we noticeably see the interaction between elements in an antenna array?
Adjacent structures affect the impedance of an antenna embedded with an array
  Resonant frequency
  Magnetic coupling in between antenna elements
impedance(p, freq);
Isolated element
impedance(l, freq);
Active element
S=sparameters(l, freq);
Full array

## Slide 32: How about we do an example to see everything we just saw in action?

## Slide 33: How do I incorporate antenna and antenna arrays into system simulations?
An isolated antenna element pattern can be imported into Phased Array system toolbox to estimate the array pattern
Phased Array System Toolbox provides algorithms and tools to design, simulate, and analyze phased array signal processing systems
  Beamforming
  Estimation of Direction of Arrival

## Slide 34: How does this tie-in with our wireless system model?

## Slide 35: Section Wrap Up
We discussed how MathWorks tools can be used in a “top-down” design workflow for antennas and antenna arrays. Specific designs tasks that we highlighted:
    Characterization, design and analysis of individual antenna elements.
    How Antenna Toolbox and Phased Array system Toolbox can be used for integrating antenna element and array behavior into system simulations.
    A methodology for determining the most efficient / effective antenna array analysis technique for a given array layout.

## Slide 36
Part Three:
  End-to-End Modelling of Wireless Systems

## Slide 37: What are we going to cover during this part of the presentation?
How top-down design can aid your MIMO system development workflow
  Study antenna array, RF, and signal processing system behaviour on baseband communication signals.
  Elaborate system models in order to systematically study subsystem and component performance impacts.
How RF and antenna element and array behavior is included in system simulations
How to include channel as well as environmental impacts on signal transmission
  Channel models and path loss capabilities in Communications System Toolbox
  Clutter, channel and free space path modeling capabilities in Phased Array System Toolbox

## Slide 38: How do MathWorks Tools Integrate into a “Top-Down” Communications System Design Flow?
INTEGRATION
IMPLEMENTATION
DESIGN
TEST & VERIFICATION
FPGA
ASIC
VHDL, Verilog
RF
SMPS
Spice-like
Algorithms
Analog
Digital
Physical
Fixed-Point
SPECIFICATION
Multi-domain algorithm development
Elaborate ‘Golden’ reference model derived from specification
Study architectural trade-offs between analog and digital systems
Determine integrated system performance
Verification
Co-simulation with 3rd party tools
Testbench generation
Integration with test and measurement equipment
Implementation and prototyping
Architectural models that are representative of board level implementations.
Synthesizable HDL code generation
Notes: How do MathWorks Tools fit in the overall mixed-signal design and verification space?
First of all, MathWorks provide a platform for system-level design and simulation. MathWorks tools are complementary to the tools used for IC implementation (Cadence, Synopsys, Mentor Graphics) and do not provide an alternative to these tools.
MathWorks tools provide a natural environment for building multi-domain system-level models, integrating analog, digital, mixed-signal, RF and supervisory logic expressed as HW or SW. A large set of libraries and a fast simulation environment make easier to build system-level models making use of graphical and textual entries for maximum expressivity.
Naturally MATLAB and Simulink provide an environment to build behavioral models and validate the real-number abstraction. These models can then be brought downstream for integration in the verification workflow.
MathWorks tools link to the downstream tools by means of cosimulation or code-generation. This supports the validation of the system-level behavioral models against the IC implementation, and allows building expressive system-level testbenches for the mixed-signal IP verification.
The link with the test and measurement equipment and the ability to use FPGAs for rapid prototyping provide even more tools for rapidly verifying the models and validate the IC.
Automatic code generation for digital HW and SW/Firmware provide a fast route towards implementation for the part of the design that support automatic model transformation (obviously not the analog part).

## Slide 39: How about we begin with a simplified system model?
Desired signal + interferer
Estimation of direction of arrival
Baseband Beamforming
Modulation error ratio
Control logic to determine the beamforming angle

## Slide 40: What parts of the system have been developed to this point?

## Slide 41: Let’s look at how we include the antenna array in the system model.
Full wave antenna array design
Antenna array model based on pattern superposition of the isolated element

## Slide 42: How do we incorporate the near-field behaviour of the array?
Antenna coupling and loading (S-parameters)
Antenna matching
Gain, IP3, NF of the RF receiver

## Slide 43: How do we incorporate individual subsystems into a larger system model? – Simulink + SimRF
What can I do with SimRF?
  Design and define both the architecture and the specs of the RF components
  Test and debug the implementation of the transceiver before going into the lab
  Integrate RF front ends with adaptive algorithms such as DPD, AGC
  Provide a model of the RF transceiver to your colleagues and customers

## Slide 44: How can I get a good trade off between Simulation Speed and Modeling Fidelity?
Deal with RF complexity while
maintaining these characteristics:
Behavioral models that capture linear, non-linear and noise performance
Ability to develop control, calibration and signal processing algorithms
Models with high levels of abstraction
Solver that allows you to use larger time-steps
Modeling fidelity
Simulation speed
True
Pass-Band
Circuit
Envelope
Equivalent
Baseband
Carrier
Signal
bandwidth
freq
Spectrum
Carrier 1
freq
Spectrum
Carrier 2
DC
freq
Spectrum
Notes: This is the spectral representation of the three modeling techniques to describe for which type of signals these simulation techniques apply.
True-pass band is suitable for ultra-wideband signals
Circuit envelope is suitable for narrowband signals over multiple simulation bandwidths.
Equivalent-baseband is suitable for narrowband signals with a single carrier.

## Slide 45: Let’s look at a typical MIMO RF Receiver architecture.
Antenna coupling and loading (S-parameters)
Antenna matching network
RF and IF Filters described with Touchstone files
IF demodulation with image rejection
Non-linearity of the amplifiers
Thermal Noise
Estimation of direction of arrival

## Slide 46: What types of channel modeling is available in MathWorks tools?
Communications System Toolbox:
  Basic channel and RF propagation models
    AWGN, Multipath Rayleigh and Rician fading and MIMO channels as well as Free Space Path Loss
LTE System Toolbox:
  Reference channels for uplink and downlink channels
WLAN System Toolbox:
  Reference and standard channels for 802.11ac and 802.11n
Phased Array System Toolbox

## Slide 47: Phased Array System Toolbox Environment based Path Loss Models
Effect of Rain
Effect of Fog
Effect of Gases
Effect of Free Space
RF Propagation modeling example available
Notes: For example, the PST has tools for modeling several RF propagation effects. These include free space path loss, atmospheric attenuation due to rain, fog and gas,

## Slide 48: Phased Array System Toolbox Field Propagation
Two-Ray Channel
Result from phased.TwoRayChannel
Notes: A two-ray channel used to analyze multipath propagation due to bounces on the ground based on the International Telecommunication Union's ITU-R specification

## Slide 49: Antenna Toolbox Field Propagation
Notes: Antenna Toolbox has a comprehensive catalog of antenna available… families of antenna include:
Dipole
Monopole
Model of helix from Antenna Toolbox, MoM solution, Field overlaid as heat map and E and H field vector plots

## Slide 50: Antenna Toolbox Antenna Pattern on a Map
Antenna field strength example available
Notes: Calculate an antenna's field strength on flat earth and display it on the web map

## Slide 51: Channel Models from Communications products
Notes: Shipping Communication channel models in CST, WLAN and LTE.

## Slide 52: From Bits to Antenna (and Back)
DSP

LNA
PA
Antenna, Antenna arrays
type of element, # elements, coupling, edge effects
Antenna Toolbox
Phased Array System Toolbox
Channel
interference, clutter, noise
Communications System Toolbox
Phased Array System Toolbox
RF Impairments
frequency dependency, non-linearity, noise, mismatches
SimRF
RF Toolbox
Waveforms
Phased Array System Toolbox
Instrument Control Toolbox
LTE System Toolbox
WLAN System Toolbox
Algorithms
beamforming, beamsteering, MIMO
Phased Array System Toolbox
Communications System Toolbox
LTE System Toolbox
WLAN System Toolbox
Simulink (Simscape)
DSP System Toolbox
Control System Toolbox
Mixed-Signal
Continuous & discrete time
DAC
TX
RX
ADC
N
N

## Slide 53: How else can MathWorks tools be used in Wireless Communications system design?
Wireless Solution web page: www.mathworks.com/wireless

## Slide 54: Wrap up
We went over the use of a new MATLAB based application, ‘RF Budget Analyzer’ and how it can be used in place of Excel spreadsheets.
We talked about how antenna element and array what-if scenarios can be explored using the MATLAB extension Antenna Toolbox.
You were showed how MathWorks tools can be used to develop a very comprehensive system model of a MIMO Communication System.

## Slide 55: Thanks for your attention Questions?

## Slide 56: Phased Array System Toolbox training course outline
Introduction
Design and analyze phased arrays
Design and Model Components of a Wireless System
Model and integrate spatial signal processing algorithms
Model antenna patterns and mutual coupling
Antenna Patterns and Mutual Coupling
Advanced Topics
Waveform Generator
Transmitter
Transmit Array
Signal Processing
Receiver
Receive Array
Environment and
Interference
Notes: Course Outline
Introduction
Phased Array Design and Analysis
Model Components of a Wireless System
Spatial Signal Processing Algorithms
Adding Antenna Patterns and Mutual Coupling
Advanced Topics
Conclusion
Appendices
Exercises
Waveform Generator
Transmitter
Transmit Array
Signal Processing
Receiver
Receive Array
Environment, Targets, and
Interference

## Slide 57: Modeling RF Systems Using MathWorks Tools Course Outline
Introduction to RF simulation using MathWorks tools
How do I model my RF system with SimRF?
Importing S-Parameters and modeling linear operation
Fundamentals of noise simulation
Modeling non-linear devices
Developing custom models
Notes: Outline of the Course
The duration of this training is 2 days, considering 7 hour of lectures and exercises and 1 hour for the breaks.
The training is divided in 6 sections:
Introduction to RF simulation using MathWorks tools.
How do I model my RF system with SimRF?
Importing S-parameters and modeling linear operation.
Fundamentals of noise simulation.
Modeling non-linear devices.
Developing custom models.

## Slide 58: Learn more about Supported Software-Defined Radios
Search: Wireless Communications Design with MATLAB
Notes: The RTL-SDR and USRPs are for IO Mode
You can use these other options for IO or for targeting
They are based on Xilinx EVM boards and the FMCOMMS boards from Analog Devices
If you want to build a real time radio prototype on an embedded platform these are good options
You can use HDL Coder to generate the HDL code

## Slide 59: What’s LTE System Toolbox?
Cell ID1
DMRS 0-2
DMRS 0-2
DMRS 1-2
LTE and LTE-Advanced (Rel-8 through Rel-12)
Scope
  FDD/TDD,
  Uplink/Downlink
  Transmitter/Receiver
~200 functions for physical layer (PHY) modeling
LTE Signal generation
ACLR/EVM measurement
Conformance Tests

## Slide 60: What is WLAN System Toolbox?
Physical layer (PHY) modeling
L-SIG, HT-SIG, VHT-SIG-A, VHT-SIG-B
OFDM, MIMO Equalization, STBC Combining
Packet detection, symbol timing correction
Coarse and fine frequency offset estimation
Preamble signal decoders for L-SIG, HT-SIG, VHT-SIG-A, VHT-SIG-B fields
Transmitter & Receiver
Standard-compliant functions for the design, simulation, analysis, and testing of wireless LAN communications systems
Packet Error Rate, EVM
Spectral Emissions
Measurements
TGn, TGac
Propagation Channel